|  | ......................... pcs. .............................. € .............................. € GEZE ECdrive T2 automatic sliding door system Automatic linear sliding door, TÜV type-tested in accordance with DIN 18650 / EN 16005, for leaf weights up to 120 kg per leaf (GCprofile Therm profile system up to 140 kg), with self-cleaning rollers for permanently smooth running. Drive Drive dimensions H x D: 100 x 190 mm Integrated rechargeable battery with automatic charge and monitoring functions for opening or closing in the event of a power failure Intelligent digital control (category 2 in accordance with DIN EN 954-1 and Performance Level “D” in accordance with DIN EN ISO 13849-1): - Convenient parameter setting, commissioning and maintenance via optional Bluetooth connection to a PC - Convenient maintenance via optional service interface: Connection to the service terminal via jack plug - Self-learning and with dynamic adaptation of the passage hold-open time for optimum convenience - Can be connected to and integrated in building systems via CAN-bus - Independent error detection and logging - Adjustment options for all door movement parameters - All functions integrated in one unit, no further modules necessary Extremely quiet DC drive Static and dynamic power limitation in accordance with DIN 18650 / EN 16005, as well as static under 150 N in accordance with ASR A1.7. Automatic reversal when an obstacle is detected Construction dimensions (in unfinished state): Clear overall height LB:............... mm Clear construction width LB:............... mm Passage height DH:.............. mm Passage height DB:.......... mm (1-leaf 700-3000 mm, 2-leaf 900-3000 mm in conjunction with GCprofile Therm 1-leaf 700-1500 mm) For sliding door elements which are planned near system limits as far as dimensions and leaf weights are concerned, a feasibility study is recommended by the manufacturer before the order is placed. Version: ( ) with single roller carriage for leaf weights up to 120 kg ( ) with double roller carriage for leaf weights up to 120 kg (note: 140 kg only in combination with GCprofile Therm) Type of installation: ( ) wall mounting or ( ) post-rail construction (façade) or ( ) girder section installation Door system version: ( ) single leaf right hand slide to open ( ) single leaf left hand slide to open ( ) double leaf ( ) with side panels ( ) with fanlight (only in combination with GCprofile Therm) Profile system: ( ) standard ISO profile fine-framed (up to 120 kg leaf weight): ( ) with 22 mm ISO glass made of ( ) ESG or ( ) LSG or ( ) mono glass fine-framed (up to 120 kg leaf weight): ( ) with 10 mm MONO glass made of ( ) ESG or ( ) LSG or ( ) ESG clamping profile (up to 120 kg leaf weight): ( ) with 10 mm ESG ( ) with 12 mm ESG or ( ) profile system GCprofile Therm (up to 140 kg leaf weight) ( ) with 32 mm ESG / 3-pane glass ( ) with 32 mm ESG / 2-pane glass Surface of the light alloy parts of the drive and the moving leaves if appropriate: ( ) anodised EV1 (E6 C-0) or ( ) RAL ........ Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 / EN 16005 by plant fitters or service partner In accordance with DIN 18650 / EN 16005: - the safety analysis must be prepared as a basis for planning and execution - an inspection must be carried out at least 1 x year and maintenance at least 1 x year |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Operation GEZE display programme switch in the AS 500 range for setting the mode of operation as well as for commissioning the drive and setting parameters, with function keys, 2x 7-segment display, alphanumerical error display, IP40 rating Modes of operation: permanently open, automatic, exit only, night-locking, off ( ) surface mounting ( ) flush mounting or GEZE keypad programme switch for setting the mode of operation, with function keys, LED dot display, coded error display, IP40 rating, suitable for switch product ranges with 55 x 55 mm switch unit Modes of operation: off, permanently open, automatic, exit only, night-locking ( ) surface mounting ( ) flush mounting or GEZE mechanical programme switch for setting the mode of operation, LED error display, IP40 rating, suitable for switch product ranges with 55 x 55 mm switch insert Modes of operation : off, permanently open, automatic, exit only, night-locking ( ) surface mounting ( ) flush mounting ( ) with rotary button ( ) with key |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the mode of operation, IP40 rating ( ) surface mounting ( ) flush mounting ( ) Euro Profile half cylinder |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 363+ combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling (..) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 365 combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 339+ active infrared detector with two light curtains for protecting the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling (..) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 341 active infrared detector with two light curtains for protecting the opening or closing area according to DIN 18650/EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE elbow switch, plastic, IP30 rating Dimensions: 90 x 180 x 23 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) surface mounting ( ) Rear panel for attaching the elbow switch to glass (in connection with transmitting module) or GEZE elbow switch, LS990, IP30 rating Dimensions: 81 x 223 x 51 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) surface mounting ( ) flush mounting or GEZE elbow switch, stainless steel, IP65 rating Dimensions: 72 x 250 x 17 mm ( ) surface mounting or GEZE non-contact proximity switch (radar) Plastic with antimicrobial surface, IP rating IP65, multi-colour LED feedback, adjustable acoustic feedback. Additional input to actively change the LED colour. Dimensions: 80 x 80 mm ( ) Flush mounting 12 mm deep ( ) Surface mounting 21 mm deep ( ) Variant for WC or GEZE LED sensor push button, plastic, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor push button, glass, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor foot switch, glass, IP69K rating Dimensions: 100 x 100 x 3 mm ( ) flush mounting ( ) vertically adjustable installation base for depths of up to 215 mm from the unfinished floor. |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE wireless programme with secure rolling code encryption for wireless activation of the drive (approx. 30 m range in the building). Transmitter: ( ) remote control with 1 push button, IP54 rating and wall fixing ( ) remote control with 2 push buttons, IP54 rating and wall fixing ( ) remote control with 4 push buttons, IP54 rating and wall fixing ( ) transmitting module for optional integration in GEZE elbow switches Receiver: ( ) receiving module with 2 outputs, 24 V, pulse mode only or pulse mode and continuous operation for mounting in the drive or in a flush-mounted socket with IP20 rating |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE GCER 300, 1-door SET Access control solution with RFID reader and PIN keypad in stand-alone operation for controlling one door (can be extended to 2 doors). RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Two authorisation types for short-time release or continuous release (office function). Configurable door release time. Variable PIN length. Communication between reader and control unit takes place by encrypted data transfer. Functions such as interlocking door system or dementia adjustable. Release buttons can be connected. Set comprising: 1 pc. GEZE GCER 300 I/O Box (ID no. 185707) 1 pc. GEZE GCVR 300 T, RFID reader flush-mounted (ID no. 185708) 2 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE GCVR Touch 300 T, RFID reader flush-mounted (ID no. 187108) GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (Id. no. 130024) or GEZE GCER 300 Light, 1-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation with a relay output for controlling one door located in the secured inner area. RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised for short-time release. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Configurable door release time. Variable PIN length. Communication takes place via encrypted data transfer. Set comprising: 1 pc. GEZE GCER 300 Light, RFID reader flush-mounted (ID no. 185710) 1 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (ID no. 130024) Accessories for GCER 300 / GCER 300 Light Plug-in power supply NT 1.0 A – 24 V DC (optional) Primary: 230 V AC, 50 Hz Secondary: 24 V DC (+/- 5 %) / 1 A (ID no. 130025) Power supply NT 1.1 A – 24 V DC flush-mounted (optional) For installation in deep standard flush-mounted boxes Primary: 230 V AC, 50 Hz Secondary: 24 V DC / 1.1 A (ID no. 151426) Power supply NT 1.5 A – 24 V DC HA (optional) For installation on top hat rails Primary: 230 V AC, 50 Hz Secondary: 21.6 – 26.4 V DC / 1.5 A (ID no. 151425) |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch external (IP54 rating) with switch function, one-sided switching operation ( ) with Euro profile half cylinder or ( ) without Euro profile half cylinder ( ) surface mounting ( ) flush mounting |

|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch external (IP54 rating) with hold-open function for fire brigade, stay-put on two sides ( ) with Euro profile half cylinder or ( ) without Euro profile half cylinder ( ) surface mounting ( ) flush mounting |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE protective leaf for protecting against shearing, nipping and trapping positions in accordance with DIN 18650 / EN 16005 in front of the moving leaf, leaves made of 10 mm ESG including door fitting, can be turned for cleaning purposes May only be used together with fine-framed moving leaf with ISO-glass. ( ) fastening on the drive or ( ) fastening on the wall alternatively: ( ) sensor-controlled fixed panel protection using 3D light curtain |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE safety leaf for protecting against shearing and nipping positions in accordance with DIN 18650 / EN 16005 with post-rail structures (depending on the offset between post surface and façade glazing) behind the moving leaf, leaf made of 10 mm ESG incl. door fitting alternatively: ( ) sensor-controlled fixed panel protection using 3D light curtain |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE emergency stop switch with lighting for switching off the mains voltage, IP20 rating An emergency control device (emergency stop switch) is not essential for compliance with DIN 18650 / EN 16005. ( ) surface mounting ( ) flush mounting |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE emergency stop switch with illuminated palm button for emergency opening or emergency unlocking, IP40 rating An emergency control device (emergency stop switch) is not essential for compliance with DIN 18650 / EN 16005. ( ) surface mounting ( ) flush mounting |
|  | ......................... pcs. .............................. € .............................. € Locking (optional position) ( ) two-stage electromagnetic locking integrated in the drive, with manual emergency unlocking or ( ) Lock M, manual hook bolt lock, prepared for Euro profile half cylinders for fine-framed moving leaves ( ) with short cylinder 32 mm (16/16) on both sides, flush with profile, lockable on both sides ( ) with Euro profile half cylinder 40 mm (30/10), lockable on one side ( ) with escutcheon plate for the installation of Euro profile half cylinder, e.g. ( ) Euro profile double cylinder on-site for integration in an on-site closing system. Note: Euro profile cylinders which project beyond the profile represent danger zones. The opening width must be restricted here. or ( ) Lock A, automatic hook bolt lock with manual emergency unlocking, for fine-framed moving leaves, quick and reliable locking and unlocking of the door in night-time operation, locking profile invisibly integrated in the profile. ( ) with 1 locking point ( ) with 2 locking points or ( ) bolt lock for installation on the underside of the moving leaf (only for fine-framed moving leaves), prepared for Euro profile cylinder or Euro profile half cylinder ( ) lockable on one side (for 46 mm Euro profile half cylinder) or ( ) lockable on both sides (for 71 mm Euro profile cylinder) |
|  | ......................... pcs. .............................. € .............................. € Floor guide (optional position) Continuous floor guide made of aluminium, anodised E6 C-0 (EV1), can be installed flush in the floor, guide rail can be removed for cleaning or replaced Recommended for external doors with opening widths greater than 2000 mm ( ) with floor guide drainage |
|  | ......................... pcs. .............................. € .............................. € Monitoring (optional position) GEZE end position sensor with Reed switch certified in accordance with VdS Class C, for installation in the sliding door drive for electronic monitoring of the door leaves (e.g. for external alarm system, building management system etc.). |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |