|  | ......................... pcs. .............................. € .............................. € GEZE TSA 325 NT RC2: Revolving door system in 3- or 4-leaf version with freely selectable inside diameter from 2500 to 3400 mm, RC2 tested in accordance with DIN 1627 – 1630, TÜV type-tested in accordance with DIN 18650, with fine frame in inviting light-coloured design, with different drive types and many possible configuration options Drive types ( ) Manual operation of the door. or ( ) Manually operated the door with GEZE speed limiter, i.e. the max. speed of rotation of the revolving door is limited by a safety mechanism in the door. or ( ) Manually operated door with GEZE automatic positioning device, i.e. the manual door is moved by a motor at very low speed after passage to the initial position/end position. Safety concept: 1 x Emergency push button in accordance with DIN EN ISO 13850 or ( ) Semi-automatic GEZE Servo drive: Increased passage comfort compared with a manual door thanks to automatic starting of the turnstile. In order to reach walking speed, the turnstile can be overridden by hand. After the door has been passed, it revolves slowly to the final position. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A Recommendation: Only if there is a constant range of users Safety concept: 1 x Emergency-stop button in accordance with DIN EN ISO 13850 or ( ) Fully automatic GEZE revolving door system (triggered via movement detector) Micro-processor controlled, electromechanical drive with infinitely adjustable speed, drive with two pre-set speeds. Complete drive with control on the interior, control in performance level "c" in accordance with DIN EN ISO 13849-1, convenient parameter setting, commissioning and after-sales service maintenance via optional Bluetooth connection to a PC, power supply: 230 V / 50 Hz / 350 W / 10 A, key programme switch for setting the operating modes. Fuse protection in accordance with DIN 18650 (TÜV type-tested and certified) comprising: - Post safety - Emergency stop push button in accordance with DIN EN ISO 13850 - Front post safety (non-contact) - Safety contact strip on the leaf, horizontal (heel protection) - Safety contact strip on the leaf, vertical (hand protection) - Coupled motion safety at the leaf (non-contact, from diameters > 3000 mm) Construction dimensions: ( ) Inside diameter: .................. ... mm (freely selectable between 2200 and 3400 mm) ( ) Clear passage height DH: .... .. mm (up to 3000 mm) ( ) Total height of door system: ............... mm ( ) Floor recess: ................ .......... mm (min. 60 mm) Note: Other dimensions on request. Model type: ( ) triple-leaf ( ) quadruple leaf Turnstile: ( ) rigid door leaf, fine-framed for mounting ESG glass. or ( ) hinged/swivelling leaf suitable for use in emergency exits rescue routes and for ventilation purposes with a canopy height of only 200 mm. Note: A suitable escape and rescue route is only achieved from an inside diameter of 2600 mm. Max. wind load 6 Beaufort. Note: Local building legislation must be complied with. Frame doorway RC2: Aluminium framework construction in the same colour as the system for installation of the doors in a façade tested to RC2 or in a wall construction built in accordance with the requirements of EN 1627. Max. width 300 mm. Top profile 100 mm. ( ) Implementation as sandwich profile ( ) Implementation as box profile Outer fine-framed drum walls made of GEZE aluminium profiles for mounting: side parts with VSG safety glass, fine-framed ( ) with VSG glass (based on P4A) 11 mm, clear Inner fine-framed drum walls made of GEZE aluminium profiles for mounting: ( ) Curved LSG 10/12 mm, clear Aluminium ceiling construction: ( ) Standard height 200 mm or ( ) Raised ceiling canopy 400 mm, with perimeter canopy cover made of curved aluminium sheets Roof covering outside: ( ) Metal cover plate or ( ) Waterproof roof with 2 water spouts (flat roof without gradient) Roof covering inside: ( ) As a dust-proof roof with wooden board or ( ) Metal cover plate Soffit: ( ) Consisting of aluminium circle elements in system colour incl. inspection opening ( ) GEZE night-time closer sliding doors running on the inside, automatic, with dead man's control and rechargeable battery package for emergency opening in the event of a power failure, with automatic rod locking, moving leaf with VSG safety glass fine-framed (up to 120 kg leaf weight) with integrated deadbolt contact: ( ) with VSG glass (based on P4A) 11 mm Surface of the light alloy parts: ( ) Powder coating according to RAL or ( ) LM anodised E6/EV1 or ( ) Colour anodised ............ Floor ring ( ) GEZE 360° stainless steel (V2A) floor ring made of rectangular tubing 30x30x2 mm. The floor ring is used as the floor covering edging at the same time. ( ) Sheet metal base 100 mm and/or ( ) Swivel flange (30x5 mm) Note: The insulation of the building is a contracted service and must be carried out on site. Floor cover ( ) GEZE clean scraping mat, anthracite colour, 22 mm, more colours available on request! or ( ) Floor cover to be carried out on site Delivery and installation Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 through plant fitters or service partner. In compliance with DIN 18650: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and after-sales service maintenance at least 1 x year |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Turnstile locking (optional position) ( ) without locking mechanism or ( ) manual locking using GEZE extended bolt lock in the door leaf, inclusive profile half cylinder or ( ) electromechanical locking (bi-stable), in the event of a power failure the door remains in the state it was in prior to the power failure. Canopy height at least 75 mm Note: When using sliding doors with night-time closers, the turnstile does not need to be locked. |
|  | ......................... pcs. .............................. € .............................. € Handles (optional position) ( ) ground, vertical stainless steel push bars, dia. 30 mm, installation directly on the glass or ( ) ground, horizontal stainless steel push bars, dia. 30 mm, installation directly on the glass |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the operating mode, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Disabled person's button (optional position) ( ) Delivery and mounting of two GEZE push buttons with wheelchair symbol in the immediate entry area of the revolving door. When this push button is actuated, the revolving speed is reduced to an adjustable value to allow handicapped persons a higher degree of access convenience and more safety. The activation duration can also be adjusted. Empty pipes must be routed to the installation point on site. Note: Use only possible with Push&Go and fully automatic versions. |
|  | ......................... pcs. .............................. € .............................. € Lighting (optional position) ( ) ..... pcs. LED spotlight (max. 1 W per light) integrated in the soffit or ( ) ..... pcs. recess for lighting to be installed on site (diameter = ..... mm) |
|  | ......................... pcs. .............................. € .............................. € Hot-air curtain system (optional position) ( ) Hot-air curtain system integrated in the suspended ceiling construction of the revolving door incl. blow-out channel in canopy area. Canopy height 400 mm Hot-air curtain system design with: ( ) Electric connection: Heat output: ............kW/ Amount of air.........m³/h ( ) Hot water connection: Heat output: ............kW/ Amount of air.........m³/h |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |