|  | ......................... pcs. .............................. € .............................. € GEZE Electrically operated opening system OL 350 EN For daily aeration and ventilation with bottom-hung, top-hung or side-hung casements1) inward opening. Compact design spindle drive E 350 N in 230 V version. Mechanical casement locking must be carried out in 1 place. Overload cut-off must be controlled electro-mechanically Technical data: Tension and pressure: 750 N Current consumption: max. 0,4A, Enclosure rating: IP 65 Ambient temperature: -20° C to +70° C Steel parts galvanised. 1) Other types of casements (pivot casement, turn casement) are possible on request Stroke: ( ) Stroke 100 mm ( ) Stroke 150 mm ( ) Stroke 200 mm ( ) Stroke 300 mm Casement size: ........ mm width ........ mm height Motor stroke: ( ) E 350/100 Casement heights: 540 – 950 mm Opening widths: approx. 380 – 390 mm ( ) E 350/150 Casement heights: 660 – 1100 mm Opening widths: approx. 550 – 530 mm ( ) E 350/200 Casement heights: 850 – 1300 mm Opening widths: approx. 670 – 610 mm ( ) E 350/300 Casement heights: 1150 – 1600 mm Opening widths: approx. 880 – 770 mm Max. casement width for wood or aluminium: 1200 mm Max. casement width for plastic: 800 mm Max. casement height: 1600 mm Min. casement height: 540 mm Specifications based on bottom-hung or top-hung casements Opening width: ........ mm (determined by the casement height and drive stroke) Panel weight max.: max. 30 kg/m² Space required on the locking side: 32 mm Space required on the motor side: 48 mm Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) RAL ........ |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Important: 1 additional hinge is required for load distribution. |
|  | ......................... pcs. .............................. € .............................. € “Open-Stop-Close” selector switch ( ) Selector switch E 27, mounted flush to wall ( ) Selector switch E 33, for surface mounting |
|  | REMARK: Electrical cable routing and connection on site by an electrical contractor according to the GEZE cable diagrams. |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |