|  | ......................... pcs. .............................. € .............................. € A4000 vector electric strike 2-pol Nearly silent opening in case of direct current, secure release of the latch, fail-secure even with high preload, can be universally used DIN right/DIN left, with radius latch which is adjustable over 3 mm in 0.75 mm catch positions, latch engagement depth: 4,5 mm, with integrated bipolar EMD protective diode, retention force: min 3000N, dimensions: 15.8 x 68.7 x 25.5 mm (W x H x D) dimensions with wireless module: 15.8 x 90.1 x 25.5 mm (W x H x D) Various electric strike variants for different safety demands: ID No. 164887 Fail-secure Fail-safe without unlocking lever with unlocking lever unlocking lever which is 2 mm longer without door status contact with door status contact Weak lock latch spring without lock latch guide with lock latch guide standard with I lock latch guide compact Momentary contact: 12-24 V AC/DC +/-15% Continuous operation: 12 V AC/DC ± 15% Momentary contact: 24-48 V AC/DC +/-15% Continuous operation: 24 V AC/DC ± 15% Continuous operation: 12 V DC with wireless receiver for 12 wireless keys Functional principle 0 3 Unlocking lever 0 1 2 Door status contact 0 1 Latch guide - - F K Voltage version A B F Without strike plate A4 - When ordering, please indicate ID No. and variant. |
| --- | --- |

|  | ......................... pcs. .............................. € .............................. € A4000 vector electric strike Nearly silent opening in case of direct current, secure release of the latch, fail-secure even with high preload, can be universally used DIN right/DIN left, with radius latch which is adjustable over 3 mm in 0.75 mm catch positions, latch engagement depth: 4,5 mm, large operating voltage range thanks to twin coil technology, with integrated bipolar EMD protective diode, retention force: min 3000N, dimensions: 15,8 x 68,7 x 25,5 mm (B x H x T) dimensions with wireless module: 15,8 x 90,1 x 25,5 mm (B x H x T) Various electric strike variants for different safety demands: ID No. 164887 Fail-secure Fail-safe without unlocking lever with unlocking lever unlocking lever which is 2 mm longer without door status contact with door status contact Weak lock latch spring without lock latch guide with lock latch guide standard with I lock latch guide compact Momentary contact: 12-24 V AC/DC +/-15% Continuous operation: 12 V AC/DC ± 15% Momentary contact: 24-48 V AC/DC +/-15% Continuous operation: 24 V AC/DC ± 15% Continuous operation: 12 V DC with wireless receiver for 12 wireless keys Functional principle 0 3 Unlocking lever 0 1 2 Door status contact 0 1 Latch guide - - F K Voltage version A B F Without strike plate A4 - When ordering, please indicate ID No. and variant. |
| --- | --- |

|  | ......................... pcs .............................. € .............................. € A5000 compact electric strike Compact dimensions, approved for use on smoke protection doors, can be universally used DIN right/DIN left, with radius latch which is adjustable over 3 mm in 0.75 mm catch positions, latch engagement depth: 6 mm large operating voltage range thanks to twin coil technology, with integrated bipolar EMD protective diode, retention force: min 3000N Dimensions: 15.8 x 59.9 x 25.5 mm (W x H x D) Dimensions with wireless module: 15.8 x 80.0 x 25.5 mm (W x H x D) Various electric strike variants for different safety demands: ID No.164888 Fail-secure Fail-safe without unlocking lever with unlocking lever unlocking lever which is 2 mm longer without door status contact with door status contact 2 mm adjusting angle door status contact with additional 2 mm adjusting angle Filling position without lock latch guide with lock latch guide Momentary contact: 6-24 V AC/DC +/-15% Continuous operation: 6 or 12 V AC/DC ± 15% Momentary contact: 12-48 V AC/DC +/-15% Continuous operation: 12 or 24 V AC/DC ± 15% Continuous operation: 12-24 V DC +/-15% signal processor and power save mode Continuous operation: 12 V DC with wireless receiver for 12 wireless keys Functional principle 0 3 Unlocking lever 0 1 2 Door status contact 0 1 2 3 Latch guide - - F Voltage version A B E F Without strike plate A5 - When ordering, please indicate ID No. and variant. |
| --- | --- |

|  | ......................... pcs .............................. € .............................. € FT500 electric strike for fire protection doors Compact dimensions, approved for use on fire protection doors, can be universally used DIN right/DIN left, with radius latch which is adjustable over 3 mm in 0.75 mm catch positions, latch engagement depth: 6,5 mm large operating voltage range thanks to twin coil technology, with integrated bipolar EMD protective diode, retention force: min 3000N Dimensions: 15.8 x 59.5 x 25.5 mm (W x H x D) Dimensions with wireless module: 15.8 x 80.0 x 25.5 mm (W x H x D) ID No. 164922 without door status contact with door status contact 2 mm adjusting angle door status contact with additional 2 mm adjusting angle Filling position without lock latch guide with lock latch guide Momentary contact: 6-24 V AC/DC +/-15% Continuous operation: 6 or 12 V AC/DC ± 15% Momentary contact: 12-48 V AC/DC +/-15% Continuous operation: 12 or 24 V AC/DC ± 15% Continuous operation: 12-24 V DC +/-15% signal processor and power save mode Continuous operation: 12 V DC with wireless receiver for 12 wireless keys Functional principle Unlocking lever Door status contact 0 1 2 3 Latch guide - - F Voltage version A B E F Without strike plate FT5 - When ordering, please indicate ID No. and variant. |
| --- | --- |