|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 5000 R-ISM/S 230 V AC, for installation on fire and smoke protection doors, in accordance with EN 1158, size 2-6 with continuous guide rail, 30 mm overall height, with integrated mechanical closing sequence control, with electric hold-open device on the passive leaf, infinitely and precisely adjustable between 80° and 130° in accordance with EN 1155, variable hold-open force, hold-open position can be overridden, vandalism protection against wilful maloperation of the closing sequence control, optionally with free swing function on the active leaf, activated through electric hold-open device by opening the door once to approx. 90°; in accordance with EN 1155, with comfort hold-open function for easy holding in place at the maximum opening angle of the free swing area to prevent the door from closing unintentionally, integrated smoke switch control unit with adaption of the alarm threshold, soiling indicator and test button, closing force, closing speed and latching action adjustable from the front, with visual closing force display, standard installation on door leaf/hinge side, with mounting plate Barrier-free in accordance with DIN 18040 For lintel heights > 1 m, 2 additional ceiling-mounted detectors are necessary. ( ) TS 5000 closer body size EN 2-6, up to leaf width 1400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1100 mm ( ) TS 5000 ECline closer body size EN 3-5, with very high efficiency > 80 % for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm ( ) retrofit kit ECline ISM/ISM BG, opening assistance for use on the active leaf, considerable drop in opening torque ( ) TS 5000 E HY 3-6 with FS lever, for free swing functions on the active leaf up to leaf width 1400 mm, a GEZE current interruption switch has to be provided ( ) TS 5000 SoftClose closer body size EN 2-6, up to leaf width 1,400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1,100 mm, quiet and safe closing even in changing pressure conditions, with one valve integrated in the closer body for the gradual adjustment of the end closing speed for braking or accelerating the door between 15° and 0° Colour: ( ) silver-coloured ( ) stainless steel optic ( ) RAL Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails Note: Please note the general building approval from DIBt (German Centre of Competence for Construction). |
| --- | --- |
|  | ......................... Pcs. .............................. € .............................. € GEZE FA GC 170 wireless extension for connecting wireless components to GEZE hold-open systems without cables, consisting of: GEZE GC 171 wireless module for connection to GEZE hold-open systems, 24 VDC supply directly via GEZE hold-open system, set up with dip switch without additional programming tools, display of connection quality and status for every device, encrypted wireless connection, wireless integration of up to six devices GC 172 / GC 173 / GC 175 tested in accordance with EN 54-25 and EN 54-18, general type approval for GEZE hold-open systems ( ) GEZE GC 172 wireless ceiling-mounted smoke detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-7 and EN 54-25, with adaption of the alarm threshold in accordance with DIN14677, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 173 wireless ceiling-mounted thermal detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-5 and EN 54-25, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 175 wireless input module for wireless connection to the GEZE GC 171 wireless module, connection to manual trigger switch or potential-free contact of a fire alarm system, encrypted wireless connection, battery operated, battery life 8 years, tested in accordance with EN 54-25 and EN 54-18, installed in flush mounted socket EN 14637 compliant, general type approval for GEZE hold-open systems |
|  | ......................... pcs. .............................. € .............................. € GEZE smoke detector GC 152, 24 V, complete with base, tested in accordance with EN 54-7, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE thermal detector GC 153, 24 V, complete with base, tested in accordance with EN 54-5, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € Ramp up wedge CB flex For use with the GEZE CB flex carry bar to prevent forcing on profile systems |
|  | ......................... pcs. .............................. € .............................. € GEZE hold-open magnets Operating voltage 24 V DC Power consumption 1.5 W Retention force 490 N ( ) Hold-open magnet basic model (zinc plated without base plate) for in-wall installation or installation in any construction ( ) Hold-open magnet for wall mounting with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface installation ( ) Base for hold-open magnet surface-mounted for floor installation ( ) Hold-open magnet with spacer tube zinc plated for floor/ceiling/wall mounting with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet for wall mounting, basic length 65 mm GEZE magnetic counter plates, ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on installation housing with damping spring for soft spring buffer for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for angle positions between door and hold-open magnet |
|  | ......................... pcs. .............................. € .............................. € GEZE current interruption switch for manual triggering ( ) surface-mounted ( ) flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Acceptance test for the hold-open system and permanent attachment of the sign of approval |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (standard) Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (optional position) with warranty extension Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months at the latest after the commissioning date) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - No separate charging for consumables up to € 25 per maintenance service - No separate charging for working hours when spare parts are replaced during the maintenance - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without additional costs (exceptions: Sundays and national holidays) - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |