|  | ......................... pc € .............................. € .............................. Mechanical self-locking panic lock set IQ lock M DL for double-leaf doors Self-locking mechanical panic lock GEZE IQ lock M DL for the moving leaf with mechanical strike box for the fixed leaf as well as all required and tested components for double-leaf full panic doors in accordance with EN 179 and EN 1125! The moving leaf is also unlocked upon panic release of the fixed leaf. Panic unlocking via latch or panic bar Self-unlocking of both door leaves Changeover function for unlocking from outside Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded; steel bolt 20 mm throw IQ lock M DL can be used for DIN left and right doors Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal and lock keep of stainless steel Supplied in a set comprising: 1 pc mechanical panic lock IQ lock M DL 1 pc mechanical strike box IQ lock DL with front metal 1 pc strike plate for receiving the lock upwards 1 pc switch lock 1 pc tubular pipe for locking upwards 1 pc solid rod for locking downwards 1 pc rod guide 1 pc floor lock hollow ( ) IQ lock M DL 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock M DL 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock M DL 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock M DL 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock M DL 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock M DL 7280 special backset 80 mm ( ) IQ lock M DL 7210 special backset 100 mm For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4to certify the durability. Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! To ensure all functions of the IQ lock M DL a door closer system with closing sequence control and a carry bar are to be fitted. GEZE recommends ( ) 2 pcs TS 5000 part no. 027333 ( ) 1 pcs ISM guide rail part no. 115549 and ( ) 2 pc GEZE panic bars (EN 1125) configurable part no. 119005 |
| --- | --- |